Pulse code modulation

Abstract

In digital communication systems, we represent discrete time signals in the form of symbols and process the signals with the help of digital signal processors. Pulse code modulation (PCM) is a method for representing analog data in their digital form and transmitting them. We can digitize all forms of analog data including full motion video, music, and virtual reality using PCM. PCM-encoded signals are in the binary form, i.e., there can be only two possible states represented by logic 1 (high) and logic 0 (low). A sine wave is sampled and quantized for PCM. The amplitude of the analog signal is sampled at regular intervals of time. First, we convert the continuous signals to their discrete form, e.g., sound waves are converted to a series of samples. This conversion is done by a process called sampling. At the source of a communication system, the amplitude of the analog signal is sampled at regular intervals of time. The next step is quantization, where the amplitude of the analog signal at each sampling is rounded off to the nearest predetermined levels. The number of levels is always a power of 2. The output of PCM is a series of binary numbers, each represented by a power of 2 bits. At the receiver end, a pulse code demodulator reconverts the binary numbers into pulses. These pulses are processed to restore the original analog waveform. The circumstances under which we can reconstruct the original signal from the sampled signal is given by the Nyquist criterion, which states that a perfect reconstruction from the sampled version is possible only if the sampling rate is more than two times the maximum frequency.

# Comments

Subject area:

The appropriate discipline-specific word choice has been used.

Language:

An advance edit ensures that unnecessarily verbose phrases are pruned.

Language:

Here we have added high and low for readers’ understanding and to clear the meaning of the values 1 and 0.

Language:

This sentence has been added to enhance the flow and transition and increase the understandability of the article.

Style:

In general, abbreviations are spelled out at their first appearance in the text as well as in the abstract, and later they are used in their abbreviated form.

Subject area:

Choosing the correct technical word to convey meaning eases readability and understanding.

Style:usagelyicleincrease the understandibd form

In academic writing, single digit numbers are preferred to be spelled out, unless they denote a value.