Pulse code modulation

Abstract

In digital communication systems, we represent discrete time signals in the form of symbols and process the signals with the help of digital signal processors. Pulse code modulation (PCM) is a method for representing analog data in their digital form and transmitting them. We can digitize all forms of analog data including full motion video, music, and virtual reality by using PCM. PCM-encoded signals are in the binary form, i, there can only be two possible states represented by logic 1 (high) and logic 0 (low). A sine wave is sampled and quantized in PCM. The amplitude of the analog signal is sampled at regular intervals of time. First, we convert continuous signals to their discrete form, e.g., sound waves were converted to a series of samples. This conversion is performed by a process called sampling. At the source of a communication system, the amplitude of the analog signal is sampled at regular intervals of time. The next step is quantization. The amplitude of the analog signal at each sampling is rounded off to the nearest predetermined level. This process is called quantization. The number of levels is always a power of 2. The output of PCM is a series of binary numbers, each represented by a certain power of 2 bits. At the receiver end, a pulse code demodulator reconverts the binary numbers into pulses. These pulses are processed to restore the original analog waveform. The circumstances under which we can completely reconstruct the original signal from the sampled signal are given by the Nyquist criterion, according to which a perfect reconstruction from the sampled version is possible only if the sampling rate is more than two times the maximum frequency.

# Comments

Word choice:

In academic writing, information is presented with accuracy and conciseness. Formal language is a hallmark of academic English.

Article Usage:

The definite article “the” has been used for better readability.

Language:

Here we have added high and low for the understanding of readers and to clarify the meaning of the values 1 and 0.

Word choice:

Choosing the right word to convey meaning eases readability and understanding.

Style:

In general, abbreviations are spelled out at their first appearance in the text as well as in the abstract, and later they are used in their abbreviated form.

Style:usagelyicleincrease the understandibd form

In general, single digit numbers are preferably spelled out, unless they denote a value.